## Slide 1
Research Implications
JMP image analysis techniques and algorithms similar to those created in this study have numerous applications in a variety of different fields, including:
Character recognition
Wildlife identification
Facial, fingerprint recognition
Topography, geological mapping
Manufacturing defect identification
Contents
Overview
Methods
Results
Discussion
Objective & Summary
The objective of this project is to use image analysis in JMP to develop an automated program for extracting metrics from skin lesion images.
First, the program segments the skin lesion outer border from the original image.
Then, algorithms extract 44 characteristic metrics from images, such as texture, symmetry, border irregularity, and variation of color, hue, saturation, luminance, and intensity.
Illustration of various variable analysis and metric extraction algorithms
Symmetry
Texture
Border Irregularity
Materials and Methods
Sample collection
Image processing
Variable analysis
Results
JMP Pro
JMP Scripting Language
The program successfully segmented lesion images and compiled metrics into a data table that can be further analyzed with statistical models.
Two applications of image analysis: fingerprint recognition and manufacturing

## Slide 2
Sample Collection
Image Processing (isolating lesion and outer border)
Image samples were collected via photography and online search.
The best images are in good focus and as close as possible to the lesion. Dermoscopy images were found to be too detailed for reliable analysis.
Automated algorithm’s main steps, starting with original image:
Detect edges using ‘canny’ filter
  Convert image to black and white – 30% red, 59% green, 11% blue
  Apply despeckle, reduce noise, and canny filters
Remove surrounding noise in four directions
  Loop through image matrix for white segments that are detached from largest white cluster
Isolate lesion outer border from four directions
  Of remaining white pixels, only keep outermost white pixel on every row and column
Crop image to fit lesion exactly
  Crop image within dimensions bounded by outermost white pixel in each direction
As needed, images were adjusted for overexposure.
Distracting features, such as the outline of an arm, were cropped out.
1 original
2 detect border
3 remove noise,
isolate border
4 overlaid image
variable analysis
Contents
Overview
Methods
Results
Discussion
Home

## Slide 3
Image Processing – Sample Code Snippets
Contents
Overview
Methods
Results
Discussion
Home
imgBW = newImage(img);
{r, g, b} = imgBW << get pixels("rgb");
i = .30*r + .59*g + .11*b;
imgBW << set pixels("rgb", {i,i,i});
imgEdge = newImage(imgBW);
imgEdge << filter("despeckle");
imgEdge << filter("despeckle");
imgEdge << filter("despeckle");
imgEdge << filter("reduce noise", 2.2);
imgEdge << filter("canny");
Detect edges
coord = J(numRows, numCols); //stores B&W RGB pixel values
table = New Table("Pixel Data", "private", //new table
newColumn("Y", set values(shape(repeat(1::numRows, numCols)`, numCols, numRows))),
newColumn("X", set values(repeat(1::numCols, numRows))),
newColumn("R", set values(r))
);
for each row(
coord[:y, :x] = :R;
); //each row has one pixel’s data
Remove surrounding noise
whiteCount = 0;
for(j = 1, j <= numCols, j++, //loop through and record all white pixels
whiteCount = 0;
for(i = 1, AND(whiteCount == 0, i <= numRows), i++,
if(coord[i, j] == 1,
whiteCount++;
insertInto(coordRow, i); //insert the white coordinate in the matrix
insertInto(coordCol, j);
);
);
);
Isolate outer border
Crop image for fit
//crop image to perfectly fit the mole, both B&W and color
onlyMole = newImage(outerBorder);
onlyMole << crop( left(le - 1), top(to - 1), bottom(bo + 1), right(ri + 1));
onlyMoleC = newImage(img);
onlyMoleC << crop(left(le - 1), top(to - 1), bottom(bo + 1), right(ri + 1));

## Slide 4
Variable Analysis – Asymmetry
Algorithm: Rotate outline image in intervals, measuring comparative distances to points on either side of center line, with a tolerance level of 5% (for the difference between each pair of distances)
Formula:
All derived metrics: average symmetry; individual rotation symmetries (sorted ascending)
Scale: 0 – 1 (least to most symmetrical)
Contents
Overview
Methods
Results
Discussion
Home
while(currentAngl <= endDegree,
  ...
  coordColRot = {}; //to store the rotated values of white pixels
  coordRowRot = {};
  //rotating the col & row values, using the 'x' shift equation for Col, 'y' shift for Row
  for(j = 1, j <= N Items(coordColShft), j++,
    insertInto(coordColRot, coordColShft[j] - midX);
    insertInto(coordRowRot, coordRowShft[j] - midY);
    coordColTemp = coordColRot[j];
    coordColRot[j] = Round((coordColRot[j] * cos(currentAngl)) + (coordRowRot[j] * sin(currentAngl)));
    coordRowRot[j] = Round((coordRowRot[j] * cos(currentAngl)) - (coordColTemp * sin(currentAngl)));
    coordColRot[j] += midX;
    coordRowRot[j] += midY;
  );
  ...
);
JMP features shown: image manipulation, matrices,
lists, mathematical functions

## Slide 5
Variable Analysis – Border Irregularity
Algorithm: Calculate slope for adjacent pairs of border pixels, counting the instances where the slope changes signs (i.e. -2, -1, 4; 2, 0, 0, -1)
All derived metrics: border irregularity count
Scale: 4 – ~100 (least to most irregular)
Contents
Overview
Methods
Results
Discussion
Home
for(j = 1, j <= 4, j++,
  match(j,
    1, endOfSide = numCols, //assign the length of the side currently being analyzed
    2, endOfSide = numCols,
    3, endOfSide = numRows,
    4, endOfSide = numRows,
    numCols
  );
  for(i = 1, AND(i < endOfSide, N Items(coordColBig) != 0), i++, //create list of all the slopes
    if(coordColBig[i] == coordColBig[i + 1],
      continue();
    );
    slope = ((coordRowBig[i + 1] - coordRowBig[i]) / (coordColBig[i + 1] - coordColBig[i]));
    insertInto(slopes, slope); //create list of all the slopes for later analysis
    totalPairs++;
  );
);
...
JMP features shown: lists, logical operators, conditional functions, mathematical functions

## Slide 6
Variable Analysis – Color Variation
Algorithm: Create ‘bins’ of small ranges for each color variable (red, green, blue, hue, luminance, saturation, intensity), 0 – 0.01, 0.01 – 0.02, etc. and count the number of significant bins (number of pixels in a variable’s bin is  average of all the buckets for that variable)
All derived metrics: maximum, minimum variation bin indices, variation value for each color variable; total variation
Scale: ~50 - ~200 (least to most variation)
Contents
Overview
Methods
Results
Discussion
Home
intens = newImage(imgBW);
intensity << crop( left(le - 1), top(to - 1), bottom(bo + 1), right(ri + 1));
{r2, g2, b2} = intens << get pixels("rgb"); //get rgb pixels of the intensity image cropped
{red, green, blue} = onlyMoleC << get pixels("rgb");
colorImgPix = onlyMoleC << get pixels(); // get rgb pixels of the color image cropped
{h, l, s} = ColorToHLS(colorImgPix); //get the HLS values of the color image
...
variation = 0;
binCtsI = J(1, numBins, 0); //counting intensity variation
binCtsH = J(1, numBins, 0); //counting hue variation
...
for(i = 1, i <= numRows, i++, //calculating variation for each type of color variable
  ...
      if(AND(r2[i, j] > (k / numBins), r2[i, j] <= ((k + 1) / numBins)),
        binCtsI[k + 1]++;
      );
...
);
JMP features shown: image functions (duplication, cropping, pixel retrieval, HLS conversion), matrices, logical operators, mathematical functions

## Slide 7
Variable Analysis – Texture
Algorithm: Calculate percentage of white pixels removed after segmenting outer border of lesion to determine how varied the interior of the lesion appears to the computer
All derived metrics: texture percentage
Formula:
Scale: 0 – 1 (least to most texture present)
Contents
Overview
Methods
Results
Discussion
Home
//all the insides become red
for(i = 1, i <= nrow(textureCoord), i++,
  for(j = 1, j <= ncol(textureCoord), j++,
    if(textureCoord[i, j] == 1,
      textureR[i, j] = 1;
    );
  );
);
//all the outsides become green
for(i = 1, i <= N Items(coordRow), i++,
  textureR[coordRow[i], coordCol[i]] = 0;
  textureG[coordRow[i], coordCol[i]] = 1;
  textureB[coordRow[i], coordCol[i]] = 0;
);
textureShown = newImage("rgb", {textureR, textureG, textureB});
textureShown << crop( left(le - 1), top(to - 1), bottom(bo + 1), right(ri + 1));
JMP features shown: image functions (creation through RGB, cropping), matrices, lists

## Slide 8
Data Table Creation, Variable Correlation and Distribution Evaluation
Contents
Overview
Methods
Results
Discussion
Automated program creates data table with all extracted metrics (sample size of 153, 44 variables), which can be used in statistical analysis
Home
Correlation scatterplots and distributions for the 5 primary variables

## Slide 9
Discussion and Future Research
Resources
After developing this program, I’d like to continue implementing new image analysis techniques in future research.
Future goals:
Improve algorithms (specifically, extract more variables from the border irregularity analysis)
Develop more JMP image analysis techniques
Support more features (batch processing analysis, etc.)
Experiment with other image analysis applications, such as character recognition and manufacturing defect identification
Julia Gong’s JMP Blog and JMP User Community Profile: http://blogs.sas.com/content/jmp/author/juliagong/
https://community.jmp.com/people/juliagong
Image samples (from Wikipedia)
Border irregularity algorithm in MatLab by Tim Kam Lee
Feature extraction in MatLab by Amran Hossen Bhuiyan, et. al.
Feature extraction in dermoscopy images by Nabin K. Mishra and M. Emre Celebi
Image segmentation in mobile devices by Luís Rosado and Maria João M. Vasconcelos
Images used in PowerPoint (fingerprint analysis, semiconductor, iPhone)
Contents
Overview
Methods
Results
Discussion
Acknowledgement
Home
I’d like to thank John Ponte and Dan Valente for their mentorship and guidance, and Diana Levey and the JMP marketing team for their support and encouragement.

## Slide 10
Figure 1
Contents
Overview
Methods
Results
Discussion
Back
Data table generated from automated metric extraction program, which can be used in statistical analysis

## Slide 11
Figure 2
Contents
Overview
Methods
Results
Discussion
Back
Partial correlation coefficients for the 5 primary variables with respect to all other variables
Given the uncorrelated nature of these variables and their small correlation coefficients, each of these variables has unique contributions to the characterizations of the images.
Correlation scatterplots and distributions for the 5 primary variables (symmetry, color variation, border irregularity, texture, and redness variation)
Correlation coefficients and partial correlation coefficients for the 5 primary variables